SUNWOOD 9281

Model No. 9281 cut type Cross cut size 2mm x 10mm sheet capacity 6 (70g/A4) power paper clip safe YES 140w staple safe YES credit card safe YES CD safe NO duty cycle/ mins 5 noise level 55 basket capacity 15 L Door Open warning Entry Ports YES 1 auto start/stop YES Auto Reverse YES speed 2mt/min paper entry width 220 mm Safety Sensor Sleep Mode YES YES auto stop on jamming YES assembled dimensions (WxDxH) 350 x240 x 460 mm

The machine is specially designed for the medium  office use.
          Automatic stop and signal start when container has been opened.
          Manual reverse paper function in case need to remove from shredding.
          Motor thermo protection
          Automatic lock photoelectric-beam cutting control and warning signal start when container is full,after 15  
          seconds the alarm release. 
          Automatic reverse switch function when the paper jammed by overload.
          Automatic start/stop photoelectric-beam cutting control
          Specially hardened solid steel cutting assemble: durable to cut paper , staples , & credit cards