SUNWOOD 9621

Model No. 9621 cut type Cross cut size 3mm x 35mm sheet capacity 21 (70g/A4) paper clip safe YES staple safe YES credit card safe YES CD safe YES duty cycle/ mins 20 noise level 58 basket capacity 30 L Door Open warning Entry Ports YES 2 auto start/stop YES Auto Reverse YES speed 3.0/min paper entry width 240 mm Safety Sensor Sleep Mode YES YES auto stop on jamming YES assembled dimensions 400X310X693mm

The machine is specially designed for the medium  office use.
          Automatic stop and signal start when container has been opened.
          Manual reverse paper function in case need to remove from shredding.
          Motor thermo protection
          Automatic lock photoelectric-beam cutting control and warning signal start when container is full,after 15  
          seconds the alarm release. 
          Automatic reverse switch function when the paper jammed by overload.
          Automatic start/stop photoelectric-beam cutting control
          Specially hardened solid steel cutting assemble: durable to cut paper , staples , & credit cards